## Slide 1
HAND GESTURE CONTROLLED ROBOT
P.Deekshith cb.sc.u4aie24039
S.Dheeraj cb.sc.u4aie24050
S.V.Dhiraj cb.sc.u4aie24052
S.Sathwik cb.sc.u4aie24051
Team Members

## Slide 2
Introduction
  Design and implement a motion-sensing and motor control system using Arduino components.
  Wirelessly control a gear motor based on motion detected by an accelerometer (ADXL335).
  Utilize an RF communication system for remote control and feedback.
Components Used:
  Arduino Uno: The main microcontroller for processing and control.
  Arduino Nano: A secondary microcontroller used for additional processing and communication.
  Motor Shield: For controlling motor direction, speed, and power.
  ADXL335 Accelerometer: To detect motion and send data to the Arduino.
  RF Pair Module: For wireless communication between devices.
  9V Battery: Powers the Arduino Uno.
  3.37V Battery with Holder: Provides power for the RF module and other components.
  Gear Motor: The actuating motor controlled based on motion sensing.

## Slide 3
CIRCUIT CONNECTIONS
1. Transmitter Section (Hand Gesture Controller)
  ADXL335 Accelerometer VCC → 3.3V, GND → GND The ADXL335 operates at 3.3V. Connecting it to 5V may damage it.
  X-axis Output A1(Arduino Nano) The accelerometer gives analog output based on tilt. A1 reads this data.
  Y-axis Output A2(Arduino Nano) The Y-axis tilt is read as an analog signal.
  Z-axis Output A3(Arduino Nano) The Z-axis value helps in detecting up/down movements.
  RF Transmitter Module VCC → 3.3V, GND → GND The RF module operates at 3.3V.
  Data Pin Digital Pin (D12) The Arduino sends movement commands as a digital signal to the RF module.
  Antenna External Wire Helps improve wireless transmission range.
2. Receiver Section (car)
  RF Receiver Module VCC → 5V, GND → GND The receiver works at 5V and needs a common ground.
  Data Pin Digital Pin (D12) The Arduino receives movement commands from the RF module here.
  Motor Driver Shield (L293D-based) Mounted on Arduino Uno The shield simplifies motor control with direct connections.
  Motor Power Supply External 9V The motors need a higher current, which the Arduino alone cannot supply.
  Motor 1 M1 (Motor Shield) One motor controls the left wheel.
  Motor 2 M2 (Motor Shield) The second motor controls the right wheel.
  Arduino Uno Power 9V Battery Provides power to the microcontroller.

## Slide 4
METHODOLOGY
  Step 1: Setting up Arduino Uno and Nano
    Configure both microcontrollers for communication and control tasks.
    The Arduino Uno processes sensor data, controls the motor, and manages communication.
    The Arduino Nano communicates wirelessly with the RF module for remote control.
  Step 2: Wiring the Components
    Connect ADXL335 accelerometer to Arduino Nano to read motion data (X, Y, Z axis).
    Mount the Motor Shield on Arduino Uno to control motor direction and speed.
    Connect Gear Motors to the Motor Shield for movement.
    Wire the RF Transmitter to Arduino Nano and the RF Receiver to Arduino Uno for wireless communication.
  Step 3: Sensor Data Acquisition
    The ADXL335 accelerometer reads real-time motion data.
    The motion data is sent to Arduino Nano for processing.

## Slide 5
  Step 4: Wireless Communication using RF Module
    The RF Transmitter (on Arduino Nano) sends movement signals.
    The RF Receiver (on Arduino Uno) receives these signals and relays them to the motor control system.
  Step 5: Motor Control Based on Motion Detection
    When specific motion (threshold value) is detected by ADXL335, Arduino Uno sends control signals to the Motor Shield.
    The Motor Shield drives the Gear Motors, making the robot move forward, backward, left, or right.
  Step 6: Power Supply
    The Arduino Uno and motors are powered by a 9V battery.
    The RF module and Arduino Nano are powered by a 3.7V battery.
  Step 7: Testing and Calibration
    Move the hand controller and check if the robot responds correctly.
    Adjust the motion sensitivity of the ADXL335 and fine-tune the motor response for accuracy.
    Ensure smooth and reliable communication between components.

## Slide 6
  The project demonstrates a successful integration of an accelerometer-based motion control system.
  The use of RF communication provides an effective wireless control solution.
  The robot’s movement is smooth and accurate, with slight adjustments required for better precision.
  The system is user-friendly and can be further enhanced with additional features like obstacle avoidance.
  The methodology followed ensures efficient, reliable, and responsive control for real-world applications.
RESULTS AND DISCUSSIONS

## Slide 7
Time Line
  As of now the arduino uno is connected to motor sheld which in turn connected to gear motors which controls the speed of the car and the direction movement is received from RF receiver
  Auduino nano should be connect to RF transmitter and ADXL335 and the motion of the car should be controlled using ESP8266 Wi-Fi Module
UID part
  In the future, we plan to integrate a Web Interface to control the car using Wi-Fi Communication.
  This will allow the user to control the car from any smartphone, laptop, or computer through a web browser.
  We will use the ESP8266 Wi-Fi Module, which will act as a server and communicate with the car

## Slide 8
THANK YOU